## Slide 1
Unified MEDS Accelerator
Sanjay Deshpande, Yongseok Lee, Mamuri Nawan, Kashif Nawaz, Ruben Niederhagen, Yunheung Paek, Jakub Szefer

## Slide 2: Modern Cryptography
Symmetric-key cryptography
Public-key cryptography
  Shor’s algorithm can potentially break existing pre-quantum public-key cryptosystems (e.g., RSA).
Post-Quantum Cryptography to the rescue!
Post-Quantum Cryptography standardization efforts are in progress around the world.
Notes: Modern cryptography forms the backbone of security in today's digital applications. It primarily comprises of symmetric key cryptography and public key cryptography.
However, the rise of quantum computing—and ongoing advances toward building quantum computers capable of breaking current cryptographic standards—pose a significant threat to pre-quantum public key cryptosystems.
A quantum algorithm called Shor’s algorithm can potentially help break existing pre-quantum public-key cryptosystems such as RSA
Post-quantum cryptography provides a beacon of hope. These algorithms run on classical computers and are believed to be quantum-secure.
Since almost just less than decade now pqc standardization efforts are in progress around the world. Organization such as NIST, ISO, IETF are helping in streamlining the processes of standardization.
Our work has been primarily on the post-quantum algorithms submitted to the NIST standardization effort.

## Slide 3: NIST Post-Quantum Cryptography Standardization
26
Round 2
Submitted candidates belong to two categories:
  PQ-KEM: Post-Quantum Key Encapsulation Mechanism
  PQ-DSS: Post-Quantum Digital Signature Scheme
Evaluation Criteria
  Security
  Hardware and Software implementation efficiency and security
  Cost (key size, signature size, etc.)
2016
Call for proposals
Round 1
2017
2018
2019
2020
2021
2022
2023
2024
2025
Round 2
Round 3
1 PQ-KEM, 3 PQ-DSS selected
4 PQ-KEM for further evaluation
Round 4
Concluded
1 PQ-KEM candidate selected
Call for proposals
Additional PQ-DSS
Round 1
69
8
40
14
ongoing
1
MEDS
Notes: The NIST standardization effort was kicked off in 2016, and cryptographers and researchers from around the world submitted their post-quantum cryptography algorithms to this multi-round competition.
The submitted algorithms belonged to two categories: PQ-KEM:post-quantum key encapsulation mechanism scheme that would help in establishing a shared secret between two parties and PQ-DSS post-quantum digital signature scheme, that would help in signing.
Round 1 of the competition kicked of with 69 candidates and as the rounds progressed the candidates were evaluated and shortlisted by round 3 – 8, candidates were selected out of which 3 signature schemes and 1 key encapsulation mechanism scheme were selected for standardization and 4 were progressed to round 4 which concluded in the last month and 1 KEM candidate was selected for standardization.
Additionally, inn 2022, an announcement for standardizing alternative pq digital signatures was made and which received 40 candidates and last year, round 2 of this competition was announced and it is ongoing.
The evaluation of these pq candidates can be broadly classified into three categories: security, hardware and software implementation efficiency and security, and cost
Our work is mainly is main focused on hardware implementation efficiency and security aspect
As per the standardization effort, standards for a few of the selected algorithms are released already and companies like Amazon, Microsoft are etc. have

## Slide 4: Motivation
Chart: 
| hawk256-ref | ov-Ip-m4f | dilithium2-m4f | mayo1-m4f | haetae2-m4f | snova-28-17-16-2-ssk-ref | cross-sha3-r-spdg-1-fast-ref | aimer-l1-param1-ref | mirith_hypercube_lafast-opt | mqom_cat1_gf251_fast-ref | perk-128-fast-5-m4 | biscuit128f-ref | sphincs-sha2-128f-simple-clean | ascon-sign128f-simple-ref | meds13220-ref
Signing | 55.8 | 135.25 | 190.75 | 455.05 | 1305.2 | 2537.95 | 1498.2 | 1619.3 | 2949.9 | 7453.7 | 8452.15 | 13703.6 | 19113.55 | 81455.55 | 88651.1
MEDS is the slowest when comparing average execution speed for signature generation and signature verification when realized on a microcontroller.
Kannwischer, M. (2024). pqm4: Benchmarking additional post-quantum signature schemes [Presentation slides]. National Institute of Standards and Technology (NIST).
Chart: 
| hawk256-ref | haetae2-m4f | ov-Ip-m4f | dilithium2-m4f | mayo1-m4f | sphincs-sha2-128s-simple-clean | snova-28-17-16-2-ssk-ref | cross-sha3-r-spdg-1-fast-ref | aimer-l1-param1-ref | ascon-sign128s-simple-ref | sphincs-a-sha2-192f-ref | mirith_hypercube_lafast-opt | perk-128-fast-5-m4 | mqom_cat1_gf251_fast-ref | biscuit128f-ref | meds13220-ref
Verification | 31.4 | 45.9 | 49.7 | 70.85 | 247.65 | 9354.55 | 959 | 1004.75 | 1555.6 | 4838.4 | 1757.3 | 2680.15 | 3905.9 | 6837.4 | 12718.55 | 88320.5

## Slide 5: Goal
Does MEDS provide sufficient inherent parallelism to accelerate the sign and verify operations on hardware to a competitive level?
To what extent can resources be shared in a combined hardware design for the sign and verify operations?
What is the overhead of supporting all security parameters at runtime, particularly concerning arithmetic in two distinct finite fields?

## Slide 6: Outline
Background
Design Choices
Evaluation and comparison against
  Software Implementation
  Other relevant hardware implementation
Key Takeaways

## Slide 7: Digital Signature Scheme
(BPK, BSK)←KeyGen(seed)
←Verify(BPK,M,S)
S←Sign(BSK,M)
Bob’s
Public Key
Bob’s
Secret Key
BPK
M,S
Message
Pass/Fail
Signature

## Slide 8: Matrix Equivalence Digital Signature Scheme (MEDS)
Security Level | Parameter Set | Finite Field q | Dimensions |  |  | w | t
 |  |  | n | m | k |  | 
L1 | MEDS-9923 | 4,093 | 14 | 14 | 14 | 14 | 1,152
 | MEDS-13220 | 4,093 | 14 | 14 | 14 | 20 | 192
L3 | MEDS-41711 | 4,093 | 22 | 22 | 22 | 26 | 608
 | MEDS-69497 | 4,093 | 22 | 22 | 22 | 36 | 160
L5 | MEDS-134180 | 2,039 | 30 | 30 | 30 | 52 | 192
 | MEDS-167717 | 2,039 | 30 | 30 | 30 | 66 | 112
A code-based digital signature scheme.
Hardness assumption : Matrix Code Equivalence (MCE) problem.
Submitted to NIST’s additional PQC digital signatures standardization process.
  Eliminated due to its low performance and novelty in security assumptions.

## Slide 9: MEDS Sign and Verify
Similar construction
(contributes 80-90% of clock cycles
Moved hash & compress inside for loop in order to save Block RAM utilization
PRNG-related operations

## Slide 10: Combined Design for Sign and Verify
Red lines show sign only path, and blue lines show verify-only path.
Both prime fields, 2039 and 4093, are close; therefore, the underlying arithmetic to support both can be designed efficiently with minimum overhead.

## Slide 11: MEDS Hardware: XOF and ExpandInv
XOF
Systemizer
PRNG
(SHAKE256)
SigmaA, SigmaB
Identity?
No
No
A & B
done?
generate B
redo
yes
e.g.,
Amxm, Bnxn
A_tilde, B_tilde
S1 - performance parameter to adjust time taken by the Systemizer at the cost of area

## Slide 12: MEDS Hardware: π = AG0B
Mat
Mul
AGB
89 | 53 | 19 | 60 | 41 | 84 | 36 | 53 | 86 | 1 | 2 | 18 | 76 | 27 | 83 | 80
46 | 96 | 31 | 58 | 77 | 1 | 83 | 27 | 72 | 10 | 3 | 50 | 27 | 88 | 19 | 43
56 | 5 | 40 | 100 | 82 | 45 | 57 | 53 | 79 | 77 | 59 | 16 | 55 | 13 | 53 | 82
82 | 26 | 45 | 94 | 86 | 82 | 83 | 30 | 54 | 90 | 65 | 67 | 70 | 13 | 6 | 97
Mat
Mul
AGB
Mat
Mul
AGB
65 | 79 | 5 | 87 | 46 | 82 | 66 | 4 | 12 | 97 | 45 | 21 | 10 | 51 | 22 | 36
13 | 23 | 33 | 11 | 82 | 51 | 38 | 38 | 13 | 62 | 91 | 74 | 80 | 32 | 27 | 98
13 | 29 | 40 | 100 | 5 | 31 | 16 | 63 | 44 | 54 | 8 | 13 | 5 | 77 | 11 | 46
61 | 27 | 2 | 59 | 60 | 2 | 37 | 84 | 9 | 86 | 98 | 41 | 45 | 92 | 10 | 89
A_tildemxm
B_tildenxn
G0kxmn
Gikxmn
S2: performance parameter to adjust time taken by the matrix multiplication at the cost of area
Smat represents another performance parameter to adjust number of matrix multiplication units running in parallel
S2

## Slide 13: MEDS Hardware: SF Systemizer
SF_Systemizer
65 | 79 | 5 | 87 | 46 | 82 | 66 | 4 | 12 | 97 | 45 | 21 | 10 | 51 | 22 | 36
13 | 23 | 33 | 11 | 82 | 51 | 38 | 38 | 13 | 62 | 91 | 74 | 80 | 32 | 27 | 98
13 | 29 | 40 | 100 | 5 | 31 | 16 | 63 | 44 | 54 | 8 | 13 | 5 | 77 | 11 | 46
61 | 27 | 2 | 59 | 60 | 2 | 37 | 84 | 9 | 86 | 98 | 41 | 45 | 92 | 10 | 89
1 | 0 | 0 | 0 | 34 | 38 | 83 | 99 | 74 | 92 | 13 | 95 | 80 | 57 | 41 | 10
0 | 1 | 0 | 0 | 14 | 7 | 65 | 53 | 60 | 91 | 28 | 93 | 67 | 52 | 38 | 42
0 | 0 | 1 | 0 | 85 | 16 | 2 | 69 | 94 | 40 | 16 | 6 | 88 | 15 | 66 | 28
0 | 0 | 0 | 1 | 33 | 27 | 46 | 86 | 32 | 85 | 37 | 79 | 15 | 8 | 85 | 51
S3 - performance parameter to adjust time taken by the Systemizer at the cost of area

## Slide 14: MEDS Hardware: Compress and Hash
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
34 | 38 | 83 | 99 | 74 | 92 | 13 | 95 | 80 | 57 | 41 | 10
14 | 7 | 65 | 53 | 60 | 91 | 28 | 93 | 67 | 52 | 38 | 42
85 | 16 | 2 | 69 | 94 | 40 | 16 | 6 | 88 | 15 | 66 | 28
33 | 27 | 46 | 86 | 32 | 85 | 37 | 79 | 15 | 8 | 85 | 51
Hash
S4 : performance parameter to adjust time taken by the hashing module

## Slide 15: Comparison of Software vs Plain Hardware Implementations
Target FPGA: Artix 7, Frequency: 113 MHz
CPU: AMD Ryzen 7 PRO 5850U, Frequency: 1,900 MHz
{S1,S2,S3,S4,Sm} = {1, 7, 6, 6, 3}
Chart: Clock Cycle Comparison
| sign | verify
Plain Hardware | 26.5 | 26.3
Optimized Software | 518.1 | 515.5
Chart: Time Comparison
| Sign | Verify
Plain Hardware | 234.2124 | 233
Optimized Software | 272 | 271
x19.5
x19.6
x1.16
x1.16

## Slide 16: The Pipelined MEDS

## Slide 17: The Pipeline

## Slide 18: The Pipeline
S1,S2,S3,S4 | Stage 1 | Stage 2 | Stage 3 | Stage 4
1 |  | 83,364 | 48,191 | 16,599
2 | 1,432 | 41,812 | 14,877 | 8,521
3 | 1,142 | 29,926 | 8,350 | 5,883
4 | 1,104 | 23,990 | 5,702 | 4,503
5 | 1,042 | 18,054 | 4,020 | 3,751
6 | 1,120 | 18,054 |  | 
7 | 980 |  | 2,477 | 2,782
8 | 1,032 | 12,118 | 2,294 | 2,522
9 | 1,084 | 12,118 | 2,153 | 2,484
10 | 1,136 | 12,118 | 2,054 | 2,371
11 | 1,188 | 12,118 | 1,955 | 2,652
12 | 1,240 | 12,118 | 1,912 | 2,197
13 | 1,292 | 12,118 | 1,869 | 2,137
14 | 975 | 6,195 | 1,643 | 1,796
3,534
12,132
3,557
3,178
Sm | Stage 2
1 | 12,132
2 | 6,066
3 | 3,033
… | …
S2= 7

## Slide 19: Evaluation – Pipelined Hardware vs Plain Hardware vs Optimized Software Implementations
{S1,S2,S3,S4,Sm} = {1, 7, 6, 6, 3}
Chart: Cycle Comparison
| Sign | Verify
Pipelined Hardware | 7.5 | 7.4
Plain Hardware | 26.5 | 26.3
CPU Optimized Software | 518.1 | 515.5
Chart: Time Comparison
| Sign | Verify
Pipelined Hardware | 67 | 66
Plain Hardware | 234 | 233
CPU Optimized Software | 272 | 271
Target FPGA: Artix 7, Frequency: 113 MHz
CPU: AMD Ryzen 7 PRO 5850U, Frequency: 1,900 MHz
x19
x20
x69
x70
x4
x4

## Slide 20: Comparison Pipelined Hardware vs Microcontroller
Chart: 
| hawk256-ref | ov-Ip-m4f | dilithium2-m4f | mayo1-m4f | haetae2-m4f | snova-28-17-16-2-ssk-ref | cross-sha3-r-spdg-1-fast-ref | aimer-l1-param1-ref | mirith_hypercube_lafast-opt | mqom_cat1_gf251_fast-ref | perk-128-fast-5-m4 | biscuit128f-ref | sphincs-sha2-128f-simple-clean | ascon-sign128f-simple-ref | meds13220-ref | meds13220-hw
Signing | 55.8 | 135.25 | 190.75 | 455.05 | 1305.2 | 2537.95 | 1498.2 | 1619.3 | 2949.9 | 7453.7 | 8452.15 | 13703.6 | 19113.55 | 81455.55 | 88651.1 | 67
Target FPGA: Artix 7, Frequency: 113 MHz
Microcontroller: Arm Cortex-M4, Frequency: 20 MHz
Kannwischer, M. (2024). pqm4: Benchmarking additional post-quantum signature schemes [Presentation slides]. National Institute of Standards and Technology (NIST).
Chart: 
| hawk256-ref | haetae2-m4f | ov-Ip-m4f | dilithium2-m4f | mayo1-m4f | sphincs-sha2-128s-simple-clean | snova-28-17-16-2-ssk-ref | cross-sha3-r-spdg-1-fast-ref | aimer-l1-param1-ref | ascon-sign128s-simple-ref | sphincs-a-sha2-192f-ref | mirith_hypercube_lafast-opt | perk-128-fast-5-m4 | mqom_cat1_gf251_fast-ref | biscuit128f-ref | meds13220-ref | meds13220-hw [OUR]
Verification | 31.4 | 45.9 | 49.7 | 70.85 | 247.65 | 9354.55 | 959 | 1004.75 | 1555.6 | 4838.4 | 1757.3 | 2680.15 | 3905.9 | 6837.4 | 12718.55 | 88320.5 | 66

## Slide 21: Efficiency of the Pipeline
Design Choice | Security Level | q | Performance Metrics |  |  |  |  | Stage-wise Idle Time % |  |  | 
 |  |  | S1 | S2 | S3 | S4 | Smat | Stage 1 | Stage 2 | Stage 3 | Stage 4
Balanced | Level I | 4,093 | 1 | 7 | 6 | 6 | 3 | 3.6% | 0.0% | 3.4% | 6.1%
 | Level III | 4,093 | 1 | 11 | 8 | 9 | 5 | 0.5% | 1.7% | 0.0% | 0.5%
 | Level V | 2,039 | 1 | 10 | 10 | 12 | 5 | 0.0% | 4.4% | 2.8% | 5.8%
 | Unified Level {1,3,5} | Both | 1 | 10 | 10 | 12 | 5 | 3.4% | 5.5% | 15.4% | 15.7%
High Performance | Level I | 4,093 | 2 | 14 | 14 | 14 | 4 | 5.7% | 3.8% | 2.4% | 0.0%
 | Level III | 4,093 | 2 | 11 | 22 | 22 | 8 | 1.5% | 0.3% | 0.0% | 3.9%
 | Level V | 2,039 | 2 | 15 | 14 | 15 | 8 | 0.2% | 2.7% | 0.6% | 0.0%
 | Unified Level {1,3,5} | both | 2 | 14 | 14 | 14 | 4 | 18.4% | 1.3% | 17.5% | 13.9%
Our hardware design architectures:
  Balanced –a balance between time and area
  High Performance –performance is a priority
 | 0% < Idle time < 10%
 | 10% < Idle time < 20%
More combinations possible

## Slide 22: Performance Comparison – NIST Security Level 1
Chart: Performance comparison of hardware implementations of different signature schemes
| MEDS-9923 [our, Bal.] | MEDS-13220 [our, Bal.] | MEDS-9923 [our, HS] | MEDS-13220 [our, HS] | ov-lp-pkc [BCH+23] | ov-V-pkc+skc [BCH+23] | MAYO 1 [SMA+24] | MAYO 1 [HSK+23] | SDitH GF256 [DHSY24] | SDitH GF251 [DHSY24] | Raccoon-128 [dPRS23] | XMSS SHA256 [WJW+19] | Dilithium-II [BNG21] | SLH-DSA (SPHINCS+)-f [DLK+25] | SLH-DSA (SPHINCS+)-s [DLK+25] | Falcon-512 [SAW+23]
Time x Area | 3.1347 | 0.432 | 2.7144 | 0.3528 | 0.03 | 2.7 | 0.6 | 0.05 | 1.6 | 4.6478 | 0.49 | 0.11 | 0.00406 | 0.2121 | 3.6364 | 0.17
Area (LUT x10^3) | 24.3 | 21.6 | 46.8 | 44.1 | 37 | 83 | 21 | 106 | 17 | 17 | 10 | 7 | 29 | 10 | 10 | 23
Time (ms) | 129 | 20 | 58 | 8 | 0.77 | 32.5 | 28.6 | 0.48 | 93.9 | 273.4 | 49.1 | 15.75 | 0.143 | 21.21 | 363.64 | 4.82
Area (x103 LUT)
Time = Sign + Verify
Target FPGA: AMD Artix 7 (except Falcon-512 – uses AMD Zynq)

## Slide 23: Goal and Key Takeaways
MEDS offers plenty of parallelism on the low level, multiplying and systemizing matrices, as well as on the high level.
When compared to sign and verify times against optimized software implementation:
Balanced design: 4-5× improvement
High-performance design: 9-10× improvement
The sign and verify loops are similar, allowing resources to be reused with minimal control logic overhead.
The overhead for additional control logic for supporting different matrix dimensions and challenge lengths is marginal.

## Slide 24: Tutorial on Security in Quantum Computing Era
Post-Quantum Cryptography to protect classical computers from Quantum Computer attacks
Security solutions to protect Quantum Computers themselves from attacks

## Slide 25: Quantum Computer Cybersecurity Resources
Quantum Computer Cybersecurity Symposium (QCCS ‘25)
Web: https://caslab.io/events/qccs

## Slide 26: Quantum Computer Cybersecurity Resources
1st International Winter School on Attacks, Defenses, and Secure Design of Quantum Computing Systems (ADSDQC ‘25)
Web: https://caslab.io/events/adsqcs
In-person, hands-on instructions and experimentation!

## Slide 27
Unified MEDS Accelerator
Thank you!

## Slide 28
Unified MEDS Accelerator
Sanjay Deshpande, Yongseok Lee, Mamuri Nawan, Kashif Nawaz, Ruben Niederhagen, Yunheung Paek, Jakub Szefer

## Slide 29: Motivation
MEDS is the slowest when comparing average execution speed for signature generation and signature verification when realized on a microcontroller.
Kannwischer, M. (2024). pqm4: Benchmarking additional post-quantum signature schemes [Presentation slides]. National Institute of Standards and Technology (NIST).