## Slide 1: Picking up the Fallen Mask: Breaking and Fixing the RS-Mask Countermeasure
Dilara Toprakhisar, Svetla Nikova, Ventzislav Nikov
13/08/2025 SAC’25
Notes: References add for CMS and all, say sth about uniformity in the beginning,
Explain the canright inversion

## Slide 2: Physical Attacks
1- Passive Attacks
Side-Channel Analysis (SCA)
  Observable leakage
    e.g., Power consumption
  Countermeasures
    Masking
  Practical evaluation
    TVLA

## Slide 3: Physical Attacks
2- Active Attacks
Fault Attacks (FA)
  Intentional disturbance of computations
    e.g., Clock/voltage glitches
  Countermeasures
    Redundancy + masking
    Random space masking (RS-Mask1)
1- K. Ramezanpour, P. Ampadu, W. Diehl: RS-Mask: Random Space Masking as an Integrated Countermeasure against Power and Fault Analysis

## Slide 4: Physical Attacks
2- Active Attacks
Fault Attacks (FA)
  Practical evaluation
    Tool based (mostly smaller gadgets)
    Overlooked vulnerabilities
      CAPA2
      CINI-MINIS gadgets3
      RS-Mask
2- O. Reparaz, L. De Meyer, B. Bilgin, V. Arribas, S. Nikova, V. Nikov, N. P. Smart: CAPA: The Spirit of Beaver Against Physical Attacks
3- J. Feldtkeller, J. Richter-Brockmann, P. Sasdrich, T. Guneysu: CINI MINIS: Domain Isolation for Fault and Combined Security

## Slide 5: RS-Mask
Goal: Maintain uniformity under fault injection
Core idea:
Protected AES
  First-order SCA
  First-order fault security
Notes: Say here what the uniformity is

## Slide 6: RS-Mask
Linear operations
  Masking is a random mapping: each share is uniform
  Faulting all but one share does not induce a bias
S-box
  Non-bijective components: any fault can induce bias
  S-box S-box
    Even if biased due to a fault, the correct value is still uniform

## Slide 7: Derivation of RS Mapping For AES S-box Inversion
Notes: Canright construction breaks the inversion into smaller subfield operations

## Slide 8: Derivation of RS Mapping for all

## Slide 9: Security of RS-Mask
Statistical fault attacks
  The mutual information between and is zero is uniform
Differential fault attacks
  Infective RS-Mask
if there is no fault

## Slide 10: Security of RS-Mask
TVLA for SCA
Distribution analysis of faulty and correct S-box outputs
SIFA simulation
  Both using a single fault location

## Slide 11: Security Analysis of RS-Mask
SIFA/DFA on four fault locations

## Slide 12: Fault Location 2 – S-box Input:
Infection mechanism is using the same S-box input
  The fault cannot be detected

## Slide 13: Fault Location 4 – Additional RS-Mask Circuit in Inversion
Any fault causes a faulty value at the input of the multiplication with
  Fault is not propagated
  Fault is propagated
If there is no difference in the repeated executions, then

## Slide 14: An AES-specific Countermeasure
Glitch extended robust -probing model4
Gate/register-faulting model5
  Correctness: the adversary may receive an incorrect output, but it remains unexploitable
  Privacy: the probability of the abort signal is independent of the secrets
4- S. Faust, V. Grosso, S. M. D. Pozo, C. Paglialonga, F. Standaert: Composable Masking Schemes in the Presence of Physical Defaults & the Robust Probing Model
5- S. Dhooghe, A. Ovchinnikov, D. Toprakhisar: StaTI: Protecting against Fault Attacks Using Stable Threshold Implementations

## Slide 15: An AES-specific Countermeasure
  Goal: uniform mapping for all inputs

## Slide 16: An AES-specific Countermeasure
In order to hide output differential:
  Additional term: which evaluates to zero if there is no fault
What about protecting the inversion?

## Slide 17: Hardware Implementation
How to protect against DFA if the input is faulted?
Duplicate the S-box input

## Slide 18: Hardware Implementation
Over three shares, based on Consolidating Masking Schemes6
Second-order SCA, first-order fault protection
  TVLA evaluation
  Fault evaluation
    Provable methods are not applicable/feasible
    Assessed the detection rate across all inputs for faulting each component in the S-box
    Assessed the distribution of output differences across all inputs and fault values
6- O. Reparaz, B. Bilgin, S. Nikova, B. Gierlichs, I. Verbauwhede: Consolidating Masking Schemes
Notes: CMS is not secure for 3rd order

## Slide 19: Conclusion
Several vulnerabilities in RS-Mask
  Insufficient evaluation
We need more comprehensive fault evaluations
An AES-specific countermeasure with a uniform mapping
Thank you!

## Slide 20: References
1- K. Ramezanpour, P. Ampadu, W. Diehl: RS-Mask: Random Space Masking as an Integrated Countermeasure against Power and Fault Analysis
2- O. Reparaz, L. De Meyer, B. Bilgin, V. Arribas, S. Nikova, V. Nikov, N. P. Smart: CAPA: The Spirit of Beaver Against Physical Attacks
3- J. Feldtkeller, J. Richter-Brockmann, P. Sasdrich, T. Guneysu: CINI MINIS: Domain Isolation for Fault and Combined Security
4- S. Faust, V. Grosso, S. M. D. Pozo, C. Paglialonga, F. Standaert: Composable Masking Schemes in the Presence of Physical Defaults & the Robust Probing Model
5- S. Dhooghe, A. Ovchinnikov, D. Toprakhisar: StaTI: Protecting against Fault Attacks Using Stable Threshold Implementations
6- O. Reparaz, B. Bilgin, S. Nikova, B. Gierlichs, I. Verbauwhede: Consolidating Masking Schemes

## Slide 21: An AES-specific Countermeasure
In order to hide output differential:
  Additional term: which evaluates to zero if there is no fault
What about protecting the inversion?

## Slide 22: Derivation of RS Mapping For AES S-box Inversion
  What if is faulty?
    The recovered output might be biased -
    Use a separate datapath to compute from the input
Notes: Canright construction breaks the inversion into smaller subfield operations

## Slide 23: Physical Attacks
2- Active Attacks
Fault Attacks (FA)
  Intentional disturbance of computations
    e.g., Clock/voltage glitches
  Countermeasures
    Redundancy + masking
    Error correction
    Error check all the critical values
    Ensure fault propagation
    Random space masking (RS-Mask1)
1- K. Ramezanpour, P. Ampadu, W. Diehl: RS-Mask: Random Space Masking as an Integrated Countermeasure against Power and Fault Analysis

## Slide 24: Physical Attacks
2- Active Attacks
Fault Attacks (FA)
  Countermeasures
    Redundancy + masking
    Error correction
    Error check all the critical values
    Ensure fault propagation
    Random space masking (RS-Mask)

## Slide 25: Physical Attacks
2- Active Attacks
Fault Attacks (FA)
  Exploitation techniques
    Wrong ciphertexts
    Correct ciphertexts
    Data-dependent fault propagation
Bit flip
ineffective fault

## Slide 26: RS-Mask
Goal: Maintain uniformity under fault injection
Core idea:
  Map variables to a random space
  Perform operations in that space
  Transform the result back to the original space
Protected AES
  First-order SCA
  First-order fault security

## Slide 27: Random Space Mapping
For a non-linear function with a random mapping and the dual mapping :
Correctness
Uniformity
Robustness
RS-Mask: S-box S-box
  Even if biased due to a fault, the correct value would still be uniform
Notes: Uniformity: should be uniform, so it maps the input to any value in the space with the same probability
Robustness: the distribution of values at the output of must be uniform under fault injection without masking
Uniformity: ℰ_1 should be uniform, so it maps the input to any value in the space with the same probability
Robustness: the distribution of values at the output of ℰ_2 must be uniform under fault injection without masking

## Slide 28: Derivation of RS Mapping For AES S-box Inversion
  Desired mapping:
  Mapping is derived for

## Slide 29: Derivation of RS Mapping for
  What if is faulty?
    The recovered output might be biased -
    Use a separate datapath to compute from the input

## Slide 30: Derivation of RS Mapping for
    Previous mapping does not hold:

## Slide 31: Hardware Implementation of RS-Mask on AES
All non-linear components: 3 share TI, one of the shares is
Linear components and key: 2 share
Area 3,5x unprotected AES, 2x TI AES

## Slide 32: An AES-specific Countermeasure
What about the inner inversion?

## Slide 33: Fault Location 1 - Kronecker Delta Function
  is added to the input
Repeat the encryption once more without fault
  If the output is different, then, or
  To differentiate in between two, repeat with different

## Slide 34: Fault Location 3 – Inversion of
  The output is infected
  is not used in the computation
  No infection
Repeat the encryption once more without fault
  If the output is different, then

## Slide 35: Hardware Implementation